CS 351 Computer Architecture                                                    Fall 2007

# Section A

### This section is closed book. Write the answers in the space provided. Each question will be weighted 3 points.

1)

Circle the correct answer.

2) Express f(A, B, C) = (A  B) V C in the sum of product form.

_________________________________________________________

3) If $r0 contained 0x39ab0f18 and $r1 contained 0x1011ffff, what is the content of register $r0 after the following instruction is executed? (Write the result in hexadecimal notation.)

addu $r0, $r1, $r0

______________________________________________________

4) Which of the following distinguish a procedure from a macro?

- a macro is a procedure that gets called very frequently

- a macro is a very short procedure

- macros do not incur the overhead when called while procedures do.

Circle the correct answer:

(1) a only   (2) a and b    (3)  c only   (4) b and c only   (5) none of them.

5) Classify each of the following instruction as R-type, I-type, J-type or pseudo-instruction.

- sll                                          _______________

- lw                                              _______________

- slt                                          _______________

- la                                             _______________

- jal                                          _______________

6) What is the range of address for unconditional jump (e.g. using the instruction j) in MIPS? Circle the correct answer.

(a) addresses to about 2^25 before the current instruction to about 2^25 after.

(b) addresses up to about 2^27 before the current instruction to about 2^27 after.

(c) addresses up to about 2^31 before the current instruction to about 2^31 after.

(d) addresses up to about 128 K before the current instruction to about 128 K after.

7) Which of the following are necessary conditions for overflow when two integers A and B (in two’s complement) are added?

(a) A < B < 0

(b) both A and B have the same sign.

(c) the sign of the sum (added as unsigned integers) is different from that of at least one of the operands.

(d) either A or B is a string of 1’s

Circle the correct answer:

(1)  a and b only (2)  b and c only (3)  b only (4)  c and d only (5) b and d only.

8) Which of the following factors most likely cause glitching?

(a) power supply

(b) propagation delay

(c) the clock source

Choose the correct answer:

- a only

- a and b only

- b only

- a and c only

- b and c only

#### Section B

This section is open-book/open-notes.

1) What does the MIPS procedure do? (Describe the mathematical relation between the input n stored in $a0 and output m stored in $v0.)                 20 points

addi    $t0,   $zero, 1

addi   $v0, $zero, 1

addi   $t2, $zero, 1

Loop:    sle    $t1, $t0, $a0

beq    $t1, $zero, Exit

sll    $t2, $t0, 1

addi   $t2, $t2, 1

add    $v0, $v0, $t2

addi   $t0, $t0, 1

j      Loop

2) (a) Write a recursive procedure count_bits in C that counts the number of 1’s in the input n, which is a 32 bit integer. Thus, count_bits(12) should return 2 since the number of 1’s in the binary representation of 12 is 2. (Make a recursive call on the number after shifting the input by one bit.)                                   9 points

(b) Translate your solution in (a) into a MIPS assembly language function.

Please add comments to every instruction of your code.                            22 points

3) A k-bit decrementer is a circuit that takes as input a k-bit (unsigned) integer x and produces a k-bit integer y such that y = x – 1. (When x is a string of k 0’s, the output will be a string of k 1’s.) Design an 8-bit decrementer using two 4-bit decrementers and as few additional logic gates as possible. Assume that there is a control input bit c to the decrementers (both 4 and 8 bits) such that the circuit decrements if c = 1, else (i.e., if c = 0) it simply outputs the input.                                                                                               17 points

4) A computer manufacturer offers two types of systems. The high-end system comes  equipped with a floating-point coprocessor while the low-end processor (without the coprocessor) uses integer-based software routines to perform the floating point operations. Both systems use a processor with the same clock speed. The high-end system has a CPI of 10 and takes 3 second to run a benchmark program, whereas the low-end system has a CPI of 6 and takes 10 seconds for the same task. (Assume that 40% of the instructions in the benchmark run on the high-end system are floating-point instructions.)

a) If the MIPS rating of the high-end system is 4.2, what is the MIPS rating of the low-end system?                                                                                                                8 points

b) What is the speed-up exhibited by the high-end system over the low-end one?  6 points

c) On average, how many integer instructions does it take to simulate a floating-point operation in the low-end system?                                                          8 points