CS 351 Computer Architecture                                         Fall 2009

Mid-Semester # 1, Oct 5, 2009

Section 1 closed-book. Write the answers in the space provided.

Name  __________________________________________________

1) In the instruction sw reg1, n (reg2), what is the range of values for n?    2 points

(a) 0 <= n <= 31

(b) -215 <= n <= 215 – 1

(c)  0  <= n <= 216 – 1

(d)  0  <= n <= 231 – 1

(e)  none of the above

2) if the clock speed of a processor is s GHz, how many millions of instructions can it execute in t seconds?                                                                               4 points

____________________________________

3) Write one instruction in MIPS assembly language that jumps to instruction labeled L if the register $to contains 0.                                                              3 points

_____________________________________

4)  If $r0 contained 0x39ab0f18 and $r1 contained 0x1011ffff, what is the content of register $r0 after the following instruction is executed? (Write the result in hexadecimal notation.)                                                                                4 points

add $r0, $r1, $r0

_________________________________

5) Which of the following statements are true about MIPS conventions regarding callers and callees?                                                                                             3 points

- a caller can never be a callee

- caller should save $a0

- callee should save $t0

Circle the correct answer:

(1) a only   (2) a and b    (3)  b only   (4) b and c only   (5) all of them

6) Classify each of the following instruction as R-type, I-type, J-type or pseudo-instruction.                                                                                                             5 points

- sra                                          _______________

- sw                                           _______________

- slez                                         _______________

- la                                            _______________

- jr                                             _______________

7) What is the range of address for unconditional jump (e.g. using the instruction j) in MIPS? Circle the correct answer. 			                                 2 points

(a) addresses to about 2^25 before the current instruction to about 2^25 after.

(b) addresses up to about 2^27 before the current instruction to about 2^27 after.

(c) addresses up to about 2^31 before the current instruction to about 2^31 after.

(d) addresses up to about 128 K before the current instruction to about 128 K after.

(e)  none of the above.

9) Which of the following are necessary conditions for overflow when two integers A and B (in two’s complement) are added?	                                 3 points

(a) A < B < 0

(b) both A and B have the same sign.

(c) the sign of the sum (added as unsigned integers) is different from that of at least one of the operands.

(d) either A or B is a string of 1’s

Circle the correct answer:

(1)  a and b only (2)  b and c only (3)  b only (4)  c and d only (5) b and d only.

10) What is the result of saturating addition of the two bytes 0x fa and 0x bc? 2 points

_________________________________

CS 351 Computer Architecture                                           Fall 2009

October 5, 2009

Open-book section

- Write a MIPS function longAdd to add 64-bit signed two-complement integers. Assume that the first number is in registers $a0 and $a1 and the second number is in registers $a2 and $a3 (even index registers contain the most significant 32 bits).  The output should be in registers $v0 and $v1 ($v0 should contain the most significant 32 bits). Your function should follow the syntax and conventions of MIPS.  (You can do this with five instructions including return statement.)                                         12 points

- The following MIPS function computes f(n) for some input integer n.

f:    addi   $t0, $zero, 1

addi   $v0, $zero, 1

addi   $t2, $zero, 1

Loop:    slt    $t1, $t0, $a0

beq    $t1, $zero, Exit

sll    $t2, $t0, 1

addi   $t2, $t2, 1

add    $v0, $v0, $t2

addi   $t0, $t0, 1

j      Loop

Exit:    jr     $ra

- Is this function a caller? Is it a callee?

(b) What is f(25)? Is f a leaf procedure?

(c)  What is the number of MIPS instructions executed to compute f(25)?                                                                   2 + 5 + 5 points

3) A computer manufacturer offers two types of systems. The high-end system comes equipped with a floating-point coprocessor while the low-end processor (without the coprocessor) uses integer-based software routines to perform the floating point operations. The high-end system uses a processor with clock speed that is 10% faster than the low-end system. The high-end system has a CPI of 8 and takes 3 second to run a benchmark program, whereas the low-end system has a CPI of 6 and takes 9 seconds for the same task. (Assume that 30% of the instructions in the benchmark run on the high-end system are floating-point instructions.)                                 2 + 4 + 6 points

a) If the MIPS rating of the high-end system is 5.1, what is the MIPS rating of the low-end system?

b) What is the speed-up exhibited by the high-end system over the low-end one?

c) On average, how many integer instructions does it take to simulate a floating-point operation in the low-end system?

- Shown below is a black box schematic diagram of a 32-bit two’s complement adder. Add additional logic gates (as few as possible) to produce an overflow bit that indicates if an overflow has occurred.                   12 points

- Assume that two out of the three registers $a0, $a1, $a2 have identical values and the third register has a different value. The following MIPS function returns the value that is different:

different: # arguments in $a0, $a1, $a2

beq $a0, $a1, its_a2

beq $a0, $a2, its_a1

move $v0, $a0

jr $ra

its_a1:   move $v0, $a1

jr $ra

its_a2:   move $v0, $a2

jr $ra

Rewrite the above function to solve this problem without using

branches.                                                                      12 points

Hint: use bitwise Boolean operations