CS 351 Computer Architecture                                           Fall 2009

Practice problems for Mid-Semester # 2, November 16, 2009

In all the problems below, FP means IEEE 754 FP format.

- Write a MIPS assembly language program that compares two FP real numbers (single precision, IEEE 754 format) stored in registers $t0 and $t1, and sets register $t2 to 0, 1 or 2 according as the result is <, > or =. Your code should not use any FP operation.

- What is the smallest positive real number that can be represented as a normalized single precision FP number?

- How many real numbers in the interval [0,1] can be exactly represented as single-precision FP numbers?

- (problem 3.27) What is the result of adding the two FP numbers 0x 0000005b and 0x 0000000b ?

- Exhibit three real numbers X, Y and Z such that using the algorithm for floating point addition presented in the text, (X + Y) + Z was not equal  X + (Y + Z).

- (problem 3.10) Find the shortest sequence of MIPS instructions to determine if there is a carry out from the addition of two registers, say registers $t3 and $t4. Place a 0 or 1 in register $t2 if the carry out is 0 or 1, respectively.

- Calculate the number of denormalized single-precision FP numbers.

- Consider the integer operations (in 2’s complement) A + B, and A – B

  - Can overflow occur if B is 0?

  - Can overflow occur if A is 0?

6.    Shown below is the block diagram of the optimized serial multiplier:

Describe the I/O relationships of the computation of the 32-bit ALU in the above diagram. Specifically, let x be the 32-bit coming from the product register, y the 32-bit multiplicand and c the 1-bit coming from control test. Let w be the 32-bit output produced. Describe the function F where w = F(x, y, c).

7. Shown below is the floating-point adder (Fig 3.16, page 254 of text):

(a) The diagram does not show the role of the sign bits of the operands. Add additional wires that show how these sign bits are used in computing the sum.

(b) One of the modules used in the above circuit is “shift right” module. How many input bits does this module get from the control unit?

(c)  Design a 1-bit shift right module controlled by a control bit b and 4 input bits. If b = 0, the output is the same as the input; if b = 1, the input should be right shifted by 1 bit. Thus, if b = 1, and the input is 0110, the output should be 0011.

(d) How many bits should be sent from the control unit to increment or decrement module? What are the largest possible increments and decrements that need to be performed?

8. What is the floating point representation of 1/3 as a single precision FP number? What are the absolute and relative errors in this representation?

9. (Exercise 3.42) With x = 0x 46d80000 and y = 0x bee00000 representing single precision FP numbers, compute x + y and x*y.

10.

11. Describe the effect that a single stuck-at-0-fault (i.e., regardless of what it should be, the signal is always 0) would have for the signals shown below in the single-cycle datapath in Figure 4.24. Which instructions, if any, will not work correctly?

(a) RegWrite = 0

(b) ALUop0 = 0

(c) Branch  = 0

(d) MemRead = 0

(e) MemWrite = 0

12) Suppose we want to add a new instruction sll $r1, ($r2) k  to the -MIPS design of Figure 4.24. Is it possible to do this without adding any new datapath wires? How should the control signals (RegWrite, ALop0, etc.) be set for this instruction?

13)

Figure 1