CS 351 Computer Architecture                                                      Fall 2009

Home Work # 5solutions

- Exercise 3.14.4, 3.14. 5, page 296 and 297

3.14.4 (a) 1/3 ( 0x 3eaaaaab, not exact

-1/7 ( 0x be924925, not exact

a + a + a results in 1.0 as expected. There are two ways to check this – one is to perform FP addition twice by hand and check that the result is 0x 3f800000. Another way to check this is to use the following MIPS code:

.text

.globl  main

main:  l.s      $f12, onethird

add.s    $f12, $f12, $f12

l.s      $f2, onethird

add.s    $f12, $f12, $f2

l.s      $f4, three

mul.s    $f2, $f4, $f2

exit:   li      $v0, 4          # print message 1

la      $a0, msg1

syscall

li      $v0, 2                   # print $f12

syscall

li      $v0,4           # print an end of line

la      $a0, cr

syscall

li   $v0, 4             # print message 2

la   $a0, msg2

syscall

mov.s $f12, $f2

li    $v0, 2

syscall

li      $v0,4           # print an end of line

la      $a0, cr

syscall

li      $v0,10          # exit

syscall

.data

onethird: .word 0x3eaaaaab

three:  .float 3.0

msg1:   .asciiz "1/3 + 1/3 + 1/3 =   "

msg2:   .asciiz "1/3 x 3 = "

cr:     .asciiz "\n"

Output from SPIM simulator confirms the result:

We leave it as an exercise to verify the result of 1/7 * 7 = 1.

- In Chapter 2, a recursive program for computing n! was presented and we noted that the largest N for which N! could be computed without overflow using 32-bit integer operations was N = 12. Rewrite the program to compute N! by performing floating-point arithmetic and show the output produced by your program for N = 100. Compute the relative error in the output.  One way to compute the relative error is to use the web site http://gmplib.org/#TRY where you can type any expression involving integers can be typed in the text box. But the result will be truncated to the nearest integer so you have to do some pre- and post-processing to get the correct result.

.text

.globl  main

main:  l.d   $f12, one

l.d   $f4,  one

l.d   $f2, hundred

addi  $t0, $zero, 100

loop:  beq   $t0, $zero, exit

mul.d $f12, $f12, $f2

addi  $t0, $t0, -1

sub.d $f2, $f2, $f4

j loop

exit:   li      $v0, 4          # print message

la      $a0, msg2

syscall

li      $v0, 3                   # print $f12

syscall

li      $v0,4           # print an end of line

la      $a0, cr

syscall

li      $v0,10          # exit

syscall

.data

hundred:   .double 100.0

one:       .double 1.0

msg2:   .asciiz "100! =   "

cr:     .asciiz "\n"

- Exercise 4.1.1 to 4.1.4

- Exercise 4.9.1 to 4.9.5